## Slide 1: Historical data and future delays estimation

## Slide 2: Model development
The model based on optimal resource optimization using Linear Programming was chosen
Platform – Excel, Simplex method
The target function: MAX number of people served by the terminal in the target week
Constrains applied (target week):
  Min number of flights granted to each airline
  Max number of flights granted to each airline
  Min number of flights assigned to each gate
  Max number of flights assigned to each gate

## Slide 3: SFO Gates - Weekly Allocation – input 1
 |  |  |  |  |  |  |  |  |  | False False False False |  |  |  |  |  | 
Number of people served: | 121701 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people served in 2015: | 121701 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people served increment: | 0% |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people delayed: | 815 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Gate usage [times a day] (9): | 9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Gate usage increase: | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Airline gate allowance increase: | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Suggested Gate Allocations: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Airlines |  | Gates |  |  |  |  |  |  |  |  |  |  |  | Flights Granted | Min Flights to assign | Max Flights to assign
Name | Code | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 |  |  | 
American Airlines | AA | 0 | 0 | 0 | 4 | 0 | 63 | 0 | 0 | 0 | 0 | 0 | 0 | 67 | 0 | 67
Alaska Airlines | AS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 26 | 0 | 26 | 0 | 26
Jetblue Airways | B6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 25 | 0 | 25 | 0 | 25
Delta Air Lines | DL | 0 | 0 | 0 | 0 | 0 | 0 | 49 | 0 | 4 | 0 | 2 | 0 | 55 | 0 | 55
Frontier Airlines | F9 | 0 | 0 | 0 | 0 | 0 | 0 | 10 | 0 | 0 | 0 | 0 | 0 | 10 | 0 | 10
Hawaiian Airlines | HA | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 0 | 0 | 0 | 0 | 0 | 3 | 0 | 3
SkyWest Airlines | OO | 0 | 0 | 0 | 44 | 0 | 0 | 0 | 63 | 59 | 0 | 0 | 0 | 166 | 0 | 166
United Airlines | UA | 0 | 63 | 0 | 15 | 35 | 0 | 0 | 0 | 0 | 63 | 0 | 63 | 239 | 0 | 239
US Airways | US | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 9 | 0 | 9 | 0 | 9
Virgin America | VX | 0 | 0 | 54 | 0 | 28 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 82 | 0 | 82
Southwest Airlines | WN | 63 | 0 | 9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 72 | 0 | 72
Flights assigned actual |  | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 62 | 63 |  |  | 
Min flights per gate allowed |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 
Max flights per gate allowed |  | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 |  |  | 

## Slide 4: SFO Gates - Weekly Allocation – input 2
Airlines Historical Behavior SFO (May-Nov): |  |  |  |  |  |  |  |  |  |  |  |  | 
Airlines |  | Reliability |  | Avg People on a flight |  | Total Flights |  | Flights weekly T1 |  | Total People |  | People Delayed | 
Name | Code |  |  |  |  |  |  |  |  |  |  |  | 
American Airlines | AA | 0.9954 |  | 218.58 |  | 14802 |  | 67 |  | 3220562 |  | 14795 | 
Alaska Airlines | AS | 0.9974 |  | 160.47 |  | 5744 |  | 26 |  | 919360 |  | 2400 | 
Jetblue Airways | B6 | 0.9980 |  | 225.16 |  | 5510 |  | 25 |  | 1238179 |  | 2471 | 
Delta Air Lines | DL | 0.9984 |  | 196.58 |  | 12179 |  | 55 |  | 2390472 |  | 3729 | 
Frontier Airlines | F9 | 1.0000 |  | 154.83 |  | 2280 |  | 10 |  | 353002 |  | 0 | 
Hawaiian Airlines | HA | 0.9922 |  | 376.45 |  | 732 |  | 3 |  | 273402 |  | 2141 | 
SkyWest Airlines | OO | 0.9919 |  | 68.41 |  | 36679 |  | 166 |  | 2488916 |  | 20222 | 
United Airlines | UA | 0.9923 |  | 192.85 |  | 52673 |  | 239 |  | 10079832 |  | 77312 | 
US Airways | US | 0.9985 |  | 290.83 |  | 1970 |  | 9 |  | 572057 |  | 871 | 
Virgin America | VX | 0.9972 |  | 169.60 |  | 18074 |  | 82 |  | 3056779 |  | 8559 | 
Southwest Airlines | WN | 0.9789 |  | 144.15 |  | 15892 |  | 72 |  | 2242581 |  | 47274 | 

## Slide 5: SFO Gates - Weekly Allocation – input 3
Gate Preferences: |  |  |  |  |  |  |  |  |  |  |  |  | 
Airlines |  | Gates |  |  |  |  |  |  |  |  |  |  | 
Name | Code | A1 | A2 | A3 | A4 | A5 | A6 | A7 | A8 | A9 | A10 | A11 | A12
American Airlines | AA | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Alaska Airlines | AS | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Jetblue Airways | B6 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Delta Air Lines | DL | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Frontier Airlines | F9 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Hawaiian Airlines | HA | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SkyWest Airlines | OO | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
United Airlines | UA | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
US Airways | US | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Virgin America | VX | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Southwest Airlines | WN | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Gate Preferences: |  |  |  |  |  |  |  |  |  |  |  |  | 
Airlines |  | Gates |  |  |  |  |  |  |  |  |  |  | 
Name | Code | A1 | A2 | A3 | A4 | A5 | A6 | A7 | A8 | A9 | A10 | A11 | A12
American Airlines | AA | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Alaska Airlines | AS | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Jetblue Airways | B6 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Delta Air Lines | DL | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Frontier Airlines | F9 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
Hawaiian Airlines | HA | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0
SkyWest Airlines | OO | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
United Airlines | UA | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0
US Airways | US | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
Virgin America | VX | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
Southwest Airlines | WN | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
Relaxed:
Restricted:

## Slide 6: Weekly Allocation: allow more flights
Number of people served: | 139364 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people served in 2015: | 121701 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people served increment: | 15% |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people delayed: | 915 | Increase: |  | 12% |  |  |  |  |  |  |  |  |  |  |  | 
Gate usage [times a day] (9): | 9 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Gate usage increase: | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Airline gate allowance increase: | 1.25 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Suggested Gate Allocations: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Airlines |  | Gates |  |  |  |  |  |  |  |  |  |  |  | Flights Granted | Min Flights to assign | Max Flights to assign
Name | Code | A1 | A2 | A3 | A4 | A5 | A6 | A7 | A8 | A9 | A10 | A11 | A12 |  |  | 
American Airlines | AA | 0 | 0 | 0 | 21 | 0 | 63 | 0 | 0 | 0 | 0 | 0 | 0 | 84 | 0 | 84
Alaska Airlines | AS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 33 | 0 | 33 | 0 | 33
Jetblue Airways | B6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 12 | 0 | 19 | 0 | 31 | 0 | 31
Delta Air Lines | DL | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 18 | 51 | 0 | 0 | 0 | 69 | 0 | 69
Frontier Airlines | F9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 13 | 0 | 0 | 0 | 0 | 13 | 0 | 13
Hawaiian Airlines | HA | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 0 | 0 | 0 | 0 | 4 | 0 | 4
SkyWest Airlines | OO | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 20 | 0 | 0 | 0 | 0 | 20 | 0 | 208
United Airlines | UA | 0 | 63 | 0 | 42 | 0 | 0 | 63 | 8 | 0 | 59 | 0 | 63 | 299 | 0 | 299
US Airways | US | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 11 | 0 | 11 | 0 | 11
Virgin America | VX | 0 | 0 | 36 | 0 | 63 | 0 | 0 | 0 | 0 | 4 | 0 | 0 | 102 | 0 | 102
Southwest Airlines | WN | 63 | 0 | 27 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 90 | 0 | 90
Flights assigned actual |  | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 |  |  | 
Min flights per gate allowed |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 
Max flights per gate allowed |  | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 | 63 |  |  | 

## Slide 7: Weekly Allocation: increase gate utilization
Number of people served: | 152127 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people served in 2015: | 121701 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people served increment: | 25% |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people delayed: | 1019 | Increase: |  | 25% |  |  |  |  |  |  |  |  |  |  |  | 
Gate usage [times a day] (9): | 12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Gate usage increase: | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Airline gate allowance increase: | 1.25 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Suggested Gate Allocations: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Airlines |  | Gates |  |  |  |  |  |  |  |  |  |  |  | Flights Granted | Min Flights to assign | Max Flights to assign
Name | Code | A1 | A2 | A3 | A4 | A5 | A6 | A7 | A8 | A9 | A10 | A11 | A12 |  |  | 
American Airlines | AA | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 84 | 0 | 0 | 84 | 0 | 84
Alaska Airlines | AS | 0 | 9 | 0 | 0 | 24 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 33 | 0 | 33
Jetblue Airways | B6 | 0 | 0 | 0 | 0 | 16 | 0 | 0 | 0 | 0 | 0 | 0 | 15 | 31 | 0 | 31
Delta Air Lines | DL | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 69 | 69 | 0 | 69
Frontier Airlines | F9 | 0 | 0 | 0 | 0 | 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 13 | 0 | 13
Hawaiian Airlines | HA | 0 | 0 | 0 | 0 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 0 | 4
SkyWest Airlines | OO | 0 | 0 | 0 | 0 | 27 | 0 | 0 | 13 | 84 | 0 | 84 | 0 | 208 | 0 | 208
United Airlines | UA | 0 | 0 | 0 | 59 | 0 | 84 | 84 | 71 | 0 | 0 | 0 | 0 | 299 | 0 | 299
US Airways | US | 0 | 11 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 11 | 0 | 11
Virgin America | VX | 0 | 0 | 78 | 25 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 102 | 0 | 102
Southwest Airlines | WN | 84 | 0 | 6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 90 | 0 | 90
Flights assigned actual |  | 84 | 20 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 |  |  | 
Min flights per gate allowed |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 
Max flights per gate allowed |  | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 |  |  | 

## Slide 8: Weekly Allocation: increase gate utilization
Number of people served: | 170940 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people served in 2015: | 121701 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people served increment: | 40% |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people delayed: | 1070 | Increase: |  | 31% |  |  |  |  |  |  |  |  |  |  |  | 
Gate usage [times a day] (9): | 12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Gate usage increase: | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Airline gate allowance increase: | 1.5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Suggested Gate Allocations: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Airlines |  | Gates |  |  |  |  |  |  |  |  |  |  |  | Flights Granted | Min Flights to assign | Max Flights to assign
Name | Code | A1 | A2 | A3 | A4 | A5 | A6 | A7 | A8 | A9 | A10 | A11 | A12 |  |  | 
American Airlines | AA | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 84 | 0 | 17 | 101 | 67 | 101
Alaska Airlines | AS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 39 | 39 | 26 | 39
Jetblue Airways | B6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 9 | 29 | 37 | 25 | 37
Delta Air Lines | DL | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 8 | 0 | 75 | 0 | 83 | 55 | 83
Frontier Airlines | F9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10 | 0 | 0 | 0 | 10 | 10 | 16
Hawaiian Airlines | HA | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5 | 0 | 0 | 0 | 5 | 3 | 5
SkyWest Airlines | OO | 0 | 0 | 0 | 0 | 0 | 21 | 0 | 84 | 61 | 0 | 0 | 0 | 166 | 166 | 250
United Airlines | UA | 0 | 0 | 44 | 84 | 84 | 63 | 84 | 0 | 0 | 0 | 0 | 0 | 358 | 239 | 358
US Airways | US | 0 | 0 | 13 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 13 | 9 | 13
Virgin America | VX | 12 | 84 | 27 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 123 | 82 | 123
Southwest Airlines | WN | 72 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 72 | 72 | 108
Flights assigned actual |  | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 |  |  | 
Min flights per gate allowed |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 
Max flights per gate allowed |  | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 |  |  | 

## Slide 9: Weekly Allocation: increase gate utilization
Number of people served: | 173332 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people served in 2015: | 121701 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people served increment: | 42% |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people delayed: | 1092 | Increase: |  | 34% |  |  |  |  |  |  |  |  |  |  |  | 
Gate usage [times a day] (9): | 12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Gate usage increase: | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Airline gate allowance increase: | 1.75 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Suggested Gate Allocations: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Airlines |  | Gates |  |  |  |  |  |  |  |  |  |  |  | Flights Granted | Min Flights to assign | Max Flights to assign
Name | Code | A1 | A2 | A3 | A4 | A5 | A6 | A7 | A8 | A9 | A10 | A11 | A12 |  |  | 
American Airlines | AA | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 84 | 0 | 33 | 117 | 67 | 117
Alaska Airlines | AS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 26 | 26 | 26 | 46
Jetblue Airways | B6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 19 | 24 | 44 | 25 | 44
Delta Air Lines | DL | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 32 | 0 | 65 | 0 | 97 | 55 | 97
Frontier Airlines | F9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 10 | 0 | 0 | 0 | 10 | 10 | 18
Hawaiian Airlines | HA | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6 | 0 | 0 | 0 | 6 | 3 | 6
SkyWest Airlines | OO | 0 | 0 | 0 | 0 | 0 | 46 | 0 | 84 | 36 | 0 | 0 | 0 | 166 | 166 | 291
United Airlines | UA | 0 | 14 | 84 | 84 | 84 | 38 | 68 | 0 | 0 | 0 | 0 | 0 | 372 | 239 | 418
US Airways | US | 0 | 0 | 0 | 0 | 0 | 0 | 16 | 0 | 0 | 0 | 0 | 0 | 16 | 9 | 16
Virgin America | VX | 12 | 70 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 82 | 82 | 143
Southwest Airlines | WN | 72 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 72 | 72 | 126
Flights assigned actual |  | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 |  |  | 
Min flights per gate allowed |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 
Max flights per gate allowed |  | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 |  |  | 

## Slide 10: Weekly Allocation: increase gate utilization
Number of people served: | 190034 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people served in 2015: | 121701 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people served increment: | 56% |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Number of people delayed: | 1199 | Increase: |  | 47% |  |  |  |  |  |  |  |  |  |  |  | 
Gate usage [times a day] (9): | 12 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Gate usage increase: | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Airline gate allowance increase: | 1.75 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Suggested Gate Allocations: |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Airlines |  | Gates |  |  |  |  |  |  |  |  |  |  |  | Flights Granted | Min Flights to assign | Max Flights to assign
Name | Code | A1 | A2 | A3 | A4 | A5 | A6 | A7 | A8 | A9 | A10 | A11 | A12 |  |  | 
American Airlines | AA | 0 | 0 | 0 | 33 | 0 | 84 | 0 | 0 | 0 | 0 | 0 | 0 | 117 | 0 | 117
Alaska Airlines | AS | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 46 | 0 | 46 | 0 | 46
Jetblue Airways | B6 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 21 | 0 | 0 | 23 | 0 | 44 | 0 | 44
Delta Air Lines | DL | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 13 | 84 | 0 | 0 | 0 | 97 | 0 | 97
Frontier Airlines | F9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 18 | 0 | 0 | 0 | 0 | 18 | 0 | 18
Hawaiian Airlines | HA | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6 | 0 | 0 | 0 | 0 | 6 | 0 | 6
SkyWest Airlines | OO | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 291
United Airlines | UA | 0 | 84 | 0 | 51 | 5 | 0 | 84 | 26 | 0 | 84 | 0 | 84 | 418 | 0 | 418
US Airways | US | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 16 | 0 | 16 | 0 | 16
Virgin America | VX | 0 | 0 | 64 | 0 | 79 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 143 | 0 | 143
Southwest Airlines | WN | 84 | 0 | 20 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 104 | 0 | 126
Flights assigned actual |  | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 |  |  | 
Min flights per gate allowed |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 
Max flights per gate allowed |  | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 | 84 |  |  | 

## Slide 11: Conclusion
Developed flexible gates assigned model base on optimal resource optimization using Linear Programming
Most significant factor for airport – better gate utilization (GU)
‘Fair’ gate distribution, 33% GU increase: +42% performance
‘Greedy’ gate distribution, 33% GU increase: +56% performance
Optimal gate distribution has limited influence (up to 8% in our test) on decrease of total delays and cancellations, it is an airlines responsibility to decrease them more.